Работа с платформой MDM9x4x

The software bootloader runtime (NPRG), launched using the SBL (download mode) interface of the MDM9x4x family platform, has an unpleasant feature. It consists in the absence of the possibility of obtaining full access to the registers of the NAND controller, which is the main condition for the operation of the qtools utilities designed for direct work with a flash drive - including qrflash and qwdirect. It is possible that it is still possible to get such access, but numerous experiments in this direction have not yet been successful.
 Regardless, launching a patched NPRG on such a platform is not completely useless. With it, at a minimum, you can read and write data - the contents of memory and platform registers - in some areas of the address space of the application processor, both using the qcommand utility commands and using the qrmem utility. In addition, such a loader allows you to launch custom applets, with which an experienced qtools user can implement almost any algorithm for working with the platform, taking into account the restrictions imposed by the restrictions on access rights to resources configured in the SBL.
One of the interesting applications of the data read / write capabilities is the ability to "programmatically" (without using "barbaric" methods like closing a point on the device board or erasing the SBL section) access to the PBL interface. For the platform family under discussion, this can be done by writing the value 1 to the BOOT_MISC_DETECT register (address 0x193d100) of the platform, followed by a reboot. Rebooting, in this case, should not be carried out in a regular way (bootloader command 0xb), but by performing an operation in the address space that causes an exception - for example, reading data at an address that does not correspond to any of the platform components, or data protected from reading.
As a result, we get such an exemplary scenario of full-fledged work with a flash drive on platforms MDM9x4x:

1. Launch NPRG, using the interface SBL:

./qdload -p/dev/ttyUSB1 -k10 -q

 Waiting for a Hello packet from the device ...

  Boot Image ID: 00000007

  Loading loaders / NPRG9x45p.bin ...

  We transfer the bootloader to the device ...

  Loader transferred successfully
Hello ok, flash memory: MT29F4G08ABBDA3W

2. We write 1 in BOOT_MISC_DETECT:

./qcommand -p/dev/ttyUSB1 -c "m 193d100 1"

3. Trying to read from a read-protected address:

./qcommand -p/dev/ttyUSB1 -c "d 7980000 4"

and interrupt the utility (at this time the system detects the PBL port):
^C

4 We launch ENPRG using the interface PBL:

./qdload -p/dev/ttyUSB2 -k10 -i

Waiting for a Hello packet from the device ...

  Image ID for boot: 0000000d

  Loading loaders / ENPRG9x45p.bin ...

  We transfer the bootloader to the device ...

  Loader transferred successfully

  HELLO protocol version: 3
  Chipset: MDM9x4x
  NAND controller base address: 079b0000
  Flash memory: Micron MT29F4G08ABBDA3W, NAND 512MiB 1.8V 8-bit
  Sector size: 516 bytes
  Page size: 2048 bytes (4 sectors)
  Pages per block: 64
  OOB size: 64 bytes
  ECC type: BCH, 4 bits
  ECC size: 7 bytes
  Spare size: 4 bytes
  Bad block marker position: user + 1d1
  Flash total size = 4096 blocks (512 MB)
Further work with a USB flash drive on this platform is performed normally.
For example, viewing the partition table:
./qrflash -p/dev/ttyUSB2 -k10 -s@ -m

 # Start End A0 A1 A2 F# Format ------ name------
============================================================
00 0 00000a ff 01 00 00 LNX 0:SBL
01 a 00000a ff 01 ff 00 LNX 0:MIBIB
02 14 0000b4 ff 01 ff 00 LNX 0:EFS2
03 c8 000008 ff 01 00 00 LNX 0:TZ
04 d0 000005 ff 01 00 00 LNX 0:RPM
05 d5 000008 ff 01 00 00 LNX 0:aboot
06 dd 000052 ff 01 00 00 LNX 0:boot
07 12f 000002 ff 01 00 00 LNX 0:SCRUB
08 131 000236 ff 01 00 00 LNX 0:modem
09 367 00000c ff 01 00 00 LNX 0:misc
10 373 000053 ff 01 00 00 LNX 0:recovery
11 3c6 000006 ff 01 00 00 LNX 0:fota_none
12 3cc 0000b6 ff 01 00 00 LNX 0:recoveryfs
13 482 000449 ff 01 00 00 LNX 0:system
14 8cb 00007c ff 01 00 00 LNX 0:PAD1
15 947 0000a2 ff 01 00 00 LNX 0:USERRW
16 9e9 0001d6 ff 01 00 00 LNX 0:HDATA
17 bbf 0003ae ff 01 00 00 LNX 0:NTGFOTA
18 f6d 000050 ff 01 00 00 LNX 0:CUST
19 fbd 000030 ff 01 00 00 LNX 0:PERSIST
============================================================
 Версия таблицы разделов: 4

Reading a section:

./qrflash -p/dev/ttyUSB2 -k10 -s@ -f1

 # начало размер A0 A1 A2 F# формат ------ Имя------
============================================================
01 a 00000a ff 01 ff 00 LNX 0:MIBIB
 * R: блок 000013 [start+009] (100%)

Section entry:

./qwdirect -p/dev/ttyUSB2 -k10 -fo -b12f pattern.bin

Record from file pattern.bin, start block 12f, size 002
  Recording mode: Linux format on a USB flash drive
  Block: 0130 Page: 3f

and so on.