Examples of using qtools
This document will collect examples of various practical problems solved using the qtools complex.

The procedure for replacing the IMEI modem

Modem IMEI is stored in nvram cell 0x226. The problem is that this cell has a write-once attribute. That is, it is registered once at the factory, and all further attempts to write to it are stupidly ignored, even without reporting an error. But we, of course, will always find a way to get around all this. To do this, you will have to roughly repeat the path along which nvram and EFS are formed at the factory. The following example is for a ZTE MF823 / 825 modem. For other modems, the procedure will probably be slightly different. In particular, the config file is only used by ZTE modems.
The sequence of actions will be as follows:

1. Merge all nvram cells from the modem:

./qnvram -ri

2. Merge the config file from the modem (for ZTE modems using this file):

./qefs -gf confg

3. We translate the modem into the boot mode and load NPRG into it, for example (for ZTE823):
./qcommand -e -c"c 3a"
./qdload -i loaders/NPRG9x15p.bin
The specific commands depend on the chipset and modem model.

4. We clean up the EFS partition. To do this, we look at its initial block and size via qrflash, and then clear it via qwdirect:

./qrflash -s@ -m
./qwdirect -b<start> -c<len>

5. Reboot the modem by pulling it out and USB and plugging it back in.
6. We enter the IMEI we need:

./qnvram -j 834001432784560

7. Replace the rest of the nvram cells:

./qnvram -wa

8. We return the config file to its place, if it was in the modem:

./qefs -wf config /

That's all. If the modem is in factory mode (with ttyUSB ports), then put it into working mode with at + zcdrun = f, and reboot it.