Qwdirect data formats

This text is a highly preliminary draft. The information in it is still incomplete and will be gradually updated.

The qwdirect program writes data from input files to a USB flash drive in various formats. This document describes the formats of input files and formats for writing to a USB flash drive.

Input files are a chain of page images that are sequentially written to a USB flash drive. The page image consists of 2 fields - data field and OOB field. Data field size:

 datasize = 512*spp

512 - the number of bytes in a sector (other sector sizes seem to not be found), spp - the number of sectors per page, depending on the type of flash drive. Usually it is either 4 or 8 sectors per page, respectively, the page size is either 2048 or 4096 bytes.
The size of the OOB field (oobsize) also depends on the type of flash drive. Usually for flash drives with 2K pages oobsize = 64, for flash drives with 4K pages oobsize = 224. This parameter is defined during the initialization of the nand controller as follows:

oobsize = (8 << ((devcfg >> 2) & 0x1)) * (pagesize >> 9);

The size of the OOB field of the input file must exactly match the auto-detect OOB size. If this is not the case, then you can force the size of the OOB field of the input file using the -z switch.

It is also possible to use input files containing only page data fields (oobsize = 0). In this case, the contents of the OOB field will be calculated automatically during recording.

The organization of data on a USB flash drive is possible in 2 versions - standard and Linux. They differ in the layout of the data on the page.
Standard format - each sector is 512 bytes in size, immediately followed by the OOB field of 16 bytes. This format is defined by the manufacturer of the flash drive and is used for all partitions, except for the file yaffs2.
Linux format - all sectors on the page except the last one are 516 bytes, followed by 12-byte OOB. The last sector on the page is 512- (4 * (spp-1)), and the next OOB is oobsize-12 * (spp-1). The extra 4 bytes of each sector contain pieces of the yaffs2 tag. Thus, the tag yaffs2 entirely falls into the data field of the flash drive and is protected by the ECC in the same way as the data itself.

Key	Format	OOB at the input	Recording fields	Format / on a flash drive
-fs	std	no	data	std
-fl	linux	no	data	linux
-fy	std	yes	data+oob	linux
-fi	std	yes	data+oob	any
-fo	std	no	data	linux